## Slide 1: Specific pollutants and priority substances in Swedish wastewater – legislation, measures and costs
Baltic Conference 2016-05-19
Peter Sörngård

## Slide 2: Legislation

## Slide 3: Swedish legislation on pollutants under EU Water Framework Directive
chemical status
  EU priority substances (Annex X)
ecological status
  EU main pollutants (Annex VIII)
  Swedish main pollutants: diclofenac, etinylestradiol and estradiol from EU watch list for priority substances (2008/105/EC, Annex III)
considered when licensing WWTPs

## Slide 4: Pharmacuticals and other organic pollutants

## Slide 5: What happens to pharmacutical residues?
most of them are emitted to water
Eg: metoprolol, trimetoprim and diclofenac
WWTP
sewage
To sludge
To water
East hospital 1 %
Sahlgrenska hospital
Housholds
Inhabitants other time of the day

## Slide 6: What happens to pharmacutical residues?
most of them are emitted to water
some comes with the sludge
Eg: fluoroquinoloner
East hospital 1 %
Sahlgrenska hospital
Housholds
Inhabitants other time of the day
sewage
WWTP
To water
To sludge

## Slide 7: What happens to pharmacutical residues?
most of them are emitted to water
some comes with the sludge
others are decomposed in the WWTP
Eg: paracetamol, ibuprofen and ketoprofen
To sludge
To water
WWTP
sewage
Inhabitants other time of the day
Housholds
Sahlgrenska hospital
East hospital 2 %

## Slide 8: Reduction of drugs in WWTP:s today
Diclofenac
Etinylestradiol
Estradiol
Ibuprofen
Diclofenac, etinylestradiol and estradiol are on the EU’s watch list but are regulated in Sweden

## Slide 9: Examples on priority pollutants in waste water
organic substances
  PFAS (cosmetics, clothes, shoes, pizzaboxes, greaseproof paper, bakery tins etc.)
  some pesticides (from stormwater)
  others listed in WFD, Annex X
heavy metals
  Hg (old sins), Cd (food), Ni, Pb, Cu (waterpipes) …

## Slide 10: Technics, strategies and estimated costs

## Slide 11: Technics tested – medical residues and other organic substances
Mechanical
-Sandfilter
-Membrane
-Activated carbone
-Filtration
-Nanofiltration
-Reverse osmosis
Chemical
-Ozone
-Ozone + hydrogenperoxid
-UV + hydrogenperoxid
-Clorine
-Clorinedioxid
-Fenton
Biological
-Active sludge
-MBBR
-Biofilm

## Slide 12: Parallel strategies are important
upstream measures (cheapest)
  reduce pharmacutical waste to sewage
  reduce use of pharmacuticals (positive also to counteract bacterial resistence)
  mandatory presciptions on critical pharmacuticals
  longterm – develop ”green” pharmacuticals
downstream measures in WWTPs
  a necessary complement

## Slide 13: Preliminary estimated costs
ozone approx. 0,05 Euro/m3
  effective on diclofenac
  reduces mikroorganisms
  reduction of particles (phosphorus) is needed
activated approx. 0,11-0,16 Euro/m3
carbon
(membrane approx. 0,54 Euro/m3)
80% reduction desirable (Switzerland)
>95 % reduction remain for many